## Slide 1: Writeup for WPICTF 2019 coffeegate by zst123 (Manzel Seet)
coffeegate
200
Hardware
Danny the intern spilled coffee on my circuit! Can you help me recover my work?
Flag is in the format flag{...}. Submit it in the format WPI{...}.
  made by John Faria
2:128

## Slide 3
A’*B’
A’*B
A*B’
A’*B’*C’
A’*B’*C
A’*B*C’
A’*B*C
A*B’*C’
A*B’*C
We see the circuit is split up into ABC and WXYZ.
Let’s get the Boolean algebra of the ABC part first

## Slide 4
  P0 = A’*B’*C’= 000
  P1 = A’*B’*C = 001
  P2 = A’*B*C’ = 010
  P3 = A’*B*C = 011
  P4 = A*B’*C’ = 100
  P5 = A*B’*C = 101
P1
P0
P0
P0
P2
P2
P2
P2
P4
P5
P3
P3
P3
Clean up the circuit.
I’ll be calling ABC as P# from now on

## Slide 5
  P0 = A’*B’*C’= 000
  P1 = A’*B’*C = 001
  P2 = A’*B*C’ = 010
  P3 = A’*B*C = 011
  P4 = A*B’*C’ = 100
  P5 = A*B’*C = 101
P1
P0
P0
P0
P2
P2
P2
P2
P4
P5
P3
P3
P3
  Don’t cares
  P6 = A*B*C’ = 110
  P7 = A*B*C = 111
  P5*W = W*A*B*C’ = W*110
I assume the circuit outputs bits of the flag.
Notice from the K-map that P5*W, P6, P7 are not used.
This leaves us with 88 bits or 11 chars of the flag.

## Slide 6
P1
P0
P0
P0
P2
P2
P2
P2
P4
P5
P3
P3
P3
P0*WXY’
P0*YZ’
(W’+X’)
P0*W’YZ’+ P0*X’YZ’
P0*Y’Z
(W+X’)
YZ
(W+X’+YZ)
P1(W+X’+YZ)
X+Y’+Z’
Y+Z
(X+Y’+Z’)(Y+Z)
P3*X
X’+Y’+Z
X’+Y+Z’
X+Y
+Z
P5(X’+Y’+Z)(X’+Y+Z’)(X+Y+Z)
P3, Y, Z’
P3, Y’, Z
P1(W+X’+YZ) (X+Y’+Z’)(Y+Z)
W’+X’+Z
W+ X’+Y’
X+Y’+Z’
X+Y+Z
P4(W’+X’+Z)(W+X’+Y’) (X+Y’+Z’)(X+Y+Z)
XZ’
P2*W’
P2*W’XZ’
P2*W’Y
X’, Y’
Z, P2
X, Y
Z’, P2
  Don’t cares
  P6 = A*B*C’ = 110
  P7 = A*B*C = 111
  P5*W = W*A*B*C’ = W*110
  P0 = A’*B’*C’= 000
  P1 = A’*B’*C = 001
  P2 = A’*B*C’ = 010
  P3 = A’*B*C = 011
  P4 = A*B’*C’ = 100
  P5 = A*B’*C = 101
Reverse the rest of the circuit.
The boxes in blue all feed into cascaded OR-gates.
Hence the final equation is the blue-equation OR-ed together.

## Slide 7
In a Python script, I printed out the truth tables based on the equations I had.
P0 and P1 corresponds to the flag format: flag{
But for P2, the circuit is incomplete.
We know the flag format flag{, hence we can deduce some bits
{ in binary is 01111011

## Slide 8
ABC = 010
0
1
1
1
1
1
1
0
Given these
P2*W’XZ’
P2*W’Y
As such,
We can fill in the bits 0111_1011
W’Y
From the flag format, we extracted 1 extra bit = W’X’Y’Z
W’XZ’
We know the flag format flag{, hence we can deduce some bits
Deduce the following:
Px=010, Sel=0000 => None # 0
Px=010, Sel=0001 => None # 1
Px=010, Sel=0010 => 1 # 1
Px=010, Sel=0011 => 1 # 1
Px=010, Sel=0100 => 1 # 1
Px=010, Sel=0101 => None # 0
Px=010, Sel=0110 => 1 # 1
Px=010, Sel=0111 => 1 # 1

## Slide 9
0
1
1
1
1
1
1
0
From this extra bit, it can’t possibly be a single bit alone.
I assume 2 possible circles (dotted):
X’Z
X’Y’Z (I chose this)
From the flag format, we extracted 1 extra bit = W’X’Y’Z
From context of the redacted circuit, I chose the 2nd option.
Left gate corresponds directly to one AND gate: X’Y’Z
Next, I assume right gate is also similar...
AND gate: XYZ’
Final result for P2
Before = (Wb * X * Zb) + (Wb * Y)
After = (Wb * X * Zb) + (Wb * Y) + (Xb*Yb*Z) + (X*Y*Zb)

## Slide 10
Updated my Python script, it gave the flag so far as flag{B
Final result for P2
Before = (Wb * X * Zb) + (Wb * Y)
After = (Wb * X * Zb) + (Wb * Y) + (Xb*Yb*Z) + (X*Y*Zb)

## Slide 11
We know P3*X is given. This is the output from the script.
From the ASCII table, the possible values are /, O, o.
Final result for P3
out = X or ((Y*Zb) ^ (Yb*Z))
The actual type of gates can be varied, but I tried and using XORs seem to produce ‘o’.

## Slide 12
  The final part is simply fill in the code for P4 and P5 which are fully given in the circuit.
  Flag is WPI{Boole}
Output from P3
Output from P4
Output from P5
Note:
The final char seems to be a ‘y’ instead of ‘}’, it seems like it is a mistake of 1 bit in the circuit.
But this mistake doesn’t affect our flag.